# STIS/CCD Acceptance Testing

Ron Downes

October 31, 2006

## Summary

A detailed acceptance test for the STIS CCD detector has been performed.  A regression test shows that BOT is giving the correct answers.  The new features (exposure expansion, pointing adjustments, actual duration usage, and visualization) are all functioning properly, and BOT can handle error conditions gracefully and provides meaningful feedback to the users.

Three issues with the Aladin display have been found – a slight misalignment of the BOT overlay with the DSS image, a failure to display all sub-exposures, and a broken link in the Aladin spreadsheet; all of these are known issues with PRs previously filed.  Only the failure to display sub-exposures is critical for release of the tool for STIS/CCD usage.

STIS ACQ exposures, although fully supported, should not be supported by  the BOT; see APT-BOT OPR 56643. This work does not need to be complete prior to the release of the tool for STIS/CCD usage.

The E1 (spectroscopic) apertures, which are supported, did not process.   This is due to the fact that these apertures were added for the last cycle of STIS, and STIS ceased operations prior to their usage.  Consequently, they were never added into BOT; see APT BOT-OPR 56645, and should be added prior to the release of BOT for STIS/CCD usage.

## Introduction

For this test, the following target and exposure was used:

Target: G191-B2B – 05h 05m 30.6119s, +52o 49’ 45.95”

(Note that this is slightly off from nominal position of the star)

Note that for the parallel observation, the following target was used:

Target: FY-COM – 12h 49m 16.00s, +27o 25’ 22.0”

Exposure: STIS/CCD, ACCUM, MIRROR, F28X50LP, 1000s

For one exposure, I used a spectroscopic mode:

Exposure: STIS/CCD, ACCUM, 52X0.5, G430L/4300, 1000s

When appropriate, modifications to the exposure (e.g. POS TARG) are detailed below.

This target/exposure was used to perform the following:

| Test | Definition |
| --- | --- |
| Regression | Comparison with old VTT/BOT |
| New features | Exposure expansion, pointing adjustment, actual duration, visualization |
| Exception Handling | Bad exposure, unsupported exposure, network query, cancel operations |

For each test, both the tabular and graphic output products are included for ease of comparison with future test results.

## Regression Test

The test exposure was run through both the VTT/BOT and the new BOT/Aladin interface.   For imaging, the VTT/BOT used a search radius of 35.4”, while the new BOT used 50.0”.  All stars found by the old VTT/BOT were found by the new BOT, while 8 additional stars were found by the new BOT (both in the extended region of the new BOT search area); the magnitudes and derived count rates were identical.  The 21 objects detected (6 Science, and 15 Unknown) were:

The field map, showing the objects found, is given below.

In the figure, the objects in boxes were found by the VTT/BOT.

A spectroscopic observation was also processed, with the VTT/BOT using a search radius of 35.4” and the new BOT using 47.4”.  All stars found by the old VTT/BOT were found by the new BOT, while 7 additional stars were found by the new BOT (both in the extended region of the new BOT search area); the magnitudes and derived count rates were identical.  The 20 objects detected (2 Science, 4 Safe, and 14 Unknown) were:

The field map, showing the objects found, is given below.

In the figure, the objects in boxes were found by the VTT/BOT.

Issues

There appears to be a slight misalignment between the BOT overlay and the DSS image, which is 0.2” in both RA and Dec.  The RA offset is consistent (the BOT overlay is always east of the star), while the Dec offset is sometimes north and sometimes south.  This discrepancy is small enough (0.2 pixels) to be of no concern, but is covered under APT-VTT PR 56217.

## New Features

### Exposure Expansion

For the STIS CCD, there are three ways for exposures to be expanded – CR-SPLIT, number of iterations greater than 1, and the use of a pattern.  The pattern case is detailed in the Pointing Adjustment section below.  For the CR-SPLIT case, a value of 3 was used, and three identical sub-exposures were created, each with one third of the nominal exposure time. For the number of iterations test, a value of 3 was used. In this case, three identical sub-exposures were generated, and BOT processing was performed on all three sub-exposures with identical results.  Aladin did display the BOT overlay, although there was only 1 image plane shown, unlike the Pattern case where each sub-exposure was its own plane.  Since the number of iterations planes would all be, by definition, identical, showing only 1 plane is acceptable (however, if the actual duration field was used, a problem could result; see below).

### Pointing Adjustment

There are 3 different types of pointing adjustments valid for the STIS CCD – POS TARG, PATTERN, and use as a PARALLEL instrument.

POS TARG

For this test, the standard exposure was modified by adding a POS TARG of X=-20” and Y=-20”.  The direction of the POS TARG is important in this test, and in order to be able to simply predict the size of the POS TARG motion, the motion must be in the same direction as the "Search Radius Vector" which is defined as the point from the fiducial to the outermost corner of the Aperture.  A selection in a different direction makes the calculation of the motion vector more complicated.

The test exposure was run through both the VTT/BOT and the new BOT/Aladin interface.   The VTT/BOT used a search radius of 35.4”, and only did analysis at the exact pointing (i.e. it assumed ORIENT=0). The new BOT increased the search radius to 77.8”, which resulted in a circle being analyzed to support any possible ORIENT value. The search radius for the new BOT without the POS TARG was 50.0”, so the increased search radius is exactly what was predicted (i.e. SQRT(20*20 + 20*20) = 28).  With the increased search radius, the new BOT analyzed more objects than the VTT/BOT, but all objects in the VTT/BOT were detected, and for those objects, the magnitudes and derived count rates were identical.

The 46 objects (11 Science, and 35 Unknown) detected were:

The field map, showing the objects found, is given below.

In the figure, the objects in boxes were found by the VTT/BOT.  The new objects are all in the area that is expected.

Pattern

For this test, the standard exposure was modified by putting it in a PATTERN (an STIS-ALONG-SLIT with 3 points with a 10” spacing at an orientation of 90o).  The orientation could not be set to be along the "Search Radius Vector", so determination of the accuracy of the search radii had to be performed be measurement in Aladin.

The test exposure was run through both the VTT/BOT and the new BOT/Aladin interface.   The VTT/BOT used a search radius of 35.4” at all three pattern points. The new BOT used different radii for its searches – one for the initial pointing (with the standard 50.0” search radius), one for the second pattern exposure (with the search radius increased to 56.0”), and one for the final pattern exposure (with a search radius of 63.6. The expanded search radius was measured to be (approximately) 54” and 62” for the second and third pattern exposure, respectively, very close to the values used by BOT. With the increased search radius, the new BOT analyzed more objects than the VTT/BOT, but all objects in the VTT/BOT were detected, and for those objects, the magnitudes and derived count rates were identical.

The 34 objects (8 Science and 26 Unknown) detected were:

The field map, showing the objects found, is given below.

In the figure, the objects in boxes were found by the VTT/BOT.  The new objects are all in the area that is expected.

Parallel

For this test, the standard exposure was modified making it be a coordinated parallel observation with a WPFC2 prime exposure.   The test exposure was run through the new BOT/Aladin interface only; the old VTT/BOT did not take the position of the parallel aperture into account when performing its checking.  The search radius used by BOT was 5.64’.  The separation between the PC and STIS/CCD is 4.85’, and after adding 0.83’ for the standard search radius, the approximate search radius BOT should have used is 5.68’, in excellent agreement with what BOT used.

A total of 206 stars were found in the new BOT, so the table below only lists the science (8) and safe objects (14). The objects detected were:

The field map, showing the objects found, is given below.

### Actual Duration

There are three ways in which the STIS CCD can use actual durations – a CR-SPLIT exposure, a pattern exposure and a number of iterations greater than 1 exposure.  For this test, the third piece of the CR-SPLIT will have the actual duration set to 500s, the second piece of a pattern will have the actual duration set to 500s, and the second of three exposures in a number of iterations=3 will have the actual duration set to 500s.

CR-SPLIT

An examination of the BOT details shows that the revised exposure time for the third piece of the pattern was indeed detected by the tool, as was evidenced by differing total counts for the targets.

Pattern

An examination of the BOT details shows that the revised exposure time for the second piece of the pattern was indeed detected by the tool, as was evidenced by differing total counts for the targets.

Number of iterations

An examination of the BOT details shows that the revised exposure time for the second sub-exposure was indeed detected by the tool.

Issue

For actual duration and number of iterations, only the first sub-exposure is shown in Aladin.  If there were different actual durations, both sub-exposures would need to be display, as they could have different answers. This is a problem is covered in APT-BOT OPR 56136, and should be corrected prior to the release of the tool for STIS/CCD usage.

### Visualization

There are many aspects to this test, all of which have already been verified by the previous ACS/SBC and ACS/HRC testing

Issue

Aladin spreadsheet name link to an external html page with more details fails for the GSC2; this is covered with APT-VTT PR 56234.

## Existing Proposals

I ran BOT on four cycle 12 (the last cycle with STIS) operational.  All ran successfully, and in a reasonable amount of time.  However, one issue was found in the testing.

Issue

STIS ACQ exposures, although fully supported, should not be supported by BOT; this is covered in APT-BOT OPR 56643.

## Exception Handling

There are four types of exception handling to be tested; Network Query Error and Cancel Ongoing Operations have been verified in the ACS/SBC testing, and Bad Exposures has been verified in the ACS/HRC testing.

### Unsupported Exposures

Given the large number of unsupported STIS apertures, I ran all (at least a representative entry for each type (e.g. for the E1 apertures, I only ran one)) supported apertures to confirm that they processed.  I also verified that the quad filter, as well as a sample of the most commonly used unsupported apertures, did not process.

Issue

The E1 (spectroscopic) apertures, which are supported, did not process.  This is due to the fact that these apertures were added for the last cycle of STIS, and STIS ceased operations prior to their usage.  Consequently, they were never added into BOT; these are covered by BOT-OPR 56645, and should be added prior to the release of BOT for STIS/CCD usage.